## Slide 1: Simplifying Exposure Index
DI Calculations

## Slide 2: Learning Objectives
Conventional Radiography
Digital Imaging
  Computed Radiography (CR)
  Digital Radiography (DR)
Exposure Indices

## Slide 3: Conventional Radiography
X-ray beam enters and exits the patient to reach the photographic film
followed by chemical processing of the film
processed image to be viewed in a view box
stored as hard copy

## Slide 4: Traditional photographic film screen systems use overall film density as an exposure indicator – direct feedback to the technologists
Underexposed
Optimum exposed
Overexposed

## Slide 5: Conventional Radiography - disadvantages
long processing time (approx. 11 minutes)
unable to enhance the images
inherent noise due to scatter which degrades the image quality
need physical storage for processed film
environmental hazard due to chemical waste

## Slide 6: Digital Imaging
an x-ray imaging technique that produces an electronic image instead of photographic film
image can be viewed, manipulated by a computer
  Digital Radiography *
  Digital fluoroscopy: first to use the digital technology
  CT
  MRI
  Ultrasound
  Nuclear medicine

## Slide 7: Digital Imaging
No need for photographic film and processing hardware
Images are
  acquired and displayed quickly
  manipulated through post-processing
  interpreted on a display monitor
  stored and retrieved via electronic methods
  transmitted electronically efficiently

## Slide 8: Digital Imaging in Routine Diagnostic Radiography
Film Digitizer
Digital Radiography
Photostimulable Phosphor Technology (CR)
Computed Radiography
Digital Fluorography
Flat Panel Detectors
(FPD) / DR
Flat panel capture detectors (TFT)
Charged coupled device (CCD)
Indirect conversion
Direct conversion

## Slide 9: Digital Imaging (PSP/CR)
Computed Radiography (CR): a cassette-based system that uses photo-stimulable phosphorus to produce radiographic images
developed by Fujifilm
process:
  expose cassette or imaging plate (IP) with x-ray
  insert into reader to be scanned by laser, and
  read and manipulate on monitor

## Slide 10: PSP (CR)
Storage Phosphor Plate (PSP)
11011101
ADC
X-RAYS
SCANNER

## Slide 11: Digital Imaging (PSP/CR)

## Slide 12: Digital Imaging (PSP/CR)

## Slide 13: Digital Imaging (FPD/DR)
Digital Radiographic (DR): a flat panel device using a x-ray absorber material coupled with a detector to make an image
  make exposure with x-ray,
  directly transfer to computer,
  read and manipulate on monitor
  it can be cassette-based (wireless portable FPD)
  it can be cassette-less (fixed detector)

## Slide 14: FPD (DR)
DETECTORS
11011101
ADC
X-RAYS
DIRECT READOUT (no laser needed)
FPD

## Slide 15: Digital Imaging - Advantages
Wide Dynamic Range: the range of shades of gray that can be displayed
High Contrast Resolution: the ability of a system to resolve adjacent structures of similar mass densities
Signal to Noise Ratio (SNR): a ratio of useful data (signal) to useless data (noise)
  dependent on mAs (a quantity of radiation exposing the patient and reaching the detector)
  Higher SNR is desirable as low SNR have a noise which makes diagnosis difficult

## Slide 16: Digital Imaging - Disadvantages
Wide dynamic range can obscure the concept of ‘correct exposure’ i.e. displayed density and exposure factors has no relation due to internal scaling
Lack of visual feedback about exposure factors
  potential for increased exposure or high dose of radiation, if unchecked
  potential for underexposure: image noise can reduce diagnostic accuracy
hence, the development of Exposure Index (EI)

## Slide 17: CR/DR systems use image processing to align the gray scale within the signals – NO feedback to the technologists

## Slide 18: Exposure Index (CR)
a feedback method developed, by Fuji films in 1980, to measure the exposure reaching digital detector
manufacturers use proprietary method with a wide variety of terminology i.e. very inconsistent and confusing
  value changes in a linear manner (Fuji, Philips, Konica-Minolta, Siemens),
    In Fuji system, it is called Sensitivity number or S#
      S# increases, exposure reduced
  value changes in a logarithmic manner (Agfa, Kodak)
    Kodak calls EI #, has direct relationship
      Value increases, exposure increases

## Slide 19: Exposure Index (CR)

## Slide 20: Exposure Index (CR)

## Slide 21: Exposure Index (CR)

## Slide 22: Standardization of Exposure Index (DR) (IEC 62494 -1)
Standardization done by:
  IEC (International Electrotechnical Commission), &
  AAPM (American Association of Physicists in Medicine) Task Group 16

## Slide 23: Exposure Index (DR)
  developed common “Exposure Indices” and “Deviation Indices” across detectors and manufacturers/vendors
purpose:
  to monitor exposure consistency (prevention of over and under exposure) within an exam type especially with initiatives of Image Gently and Image Wisely using ALARA principle
  producing image of accepting quality

## Slide 24: Exposure Index (DR)
consists of three values
  Exposure Index (EI):
    is a measure of radiation in the relevant image region on the receptor
    is a function of the region of interest (ROI) selected by the digital radiography workstation for the examination type, image processing, and exposure used
    is linear in relation to detector exposure i.e. double the mAs means double the EI

## Slide 25: Exposure Index (DR)
consists of three values
  Target Exposure Index (EIT):
    is the reference exposure value obtained for each exam type using the statistical average of 50 exposures
    set by the manufacturer or by the local imaging center
    is dependent on the body part, view, procedure, and imaging receptor

## Slide 26: Exposure Index (DR)
consists of three values
  Deviation Index (DI):
    quantifies how much the actual EI varies from the EIT, defined by the following formula
    b = body part, v = view
    a good indicator of under and over exposure
    3 deviation units equals 2x exposure or ½ exposure (+3 or -3)
      DI = 0 when EI = EIT
      DI = +3.0 i.e. 2 x EIT
      DI = -3.0 i.e. ½ x EIT

## Slide 27: Exposure Index & Patient Dose
EI can not calculate or is not related to patient dose
patient dose is related to the followings:
  patient body habitus
  detector type
  type of filters used
  use of collimation
  use of grid

## Slide 28: Exposure Index (DR) - AGFA
3 colors Dose-Bar graph which helps radiologic technologist to monitor the exposure technique quality personally
Color improves the interpretation of lgM/DI
  Green: within range
  Yellow: slightly over or slightly under exposure
  Red: significantly over or significantly under exposure

## Slide 29: Exposure Index (DR) - AGFA
-3 < D.I. < +3
Green bar
-6 < D.I. < -3 or
+ 3 < D.I. < +6
Yellow bar
D.I. < -6 or
+6 < D.I
Red bar

## Slide 30: Exposure Index (DR) - AGFA

## Slide 31: Technique Compensastion using EI and TEI

## Slide 32: Technique Compensastion using DI
D 4.0
oldmAs
newmAs
Exposure Factor
Exposure Factor
Exposure Factor
Exposure Factor

## Slide 33
)

## Slide 34: Exposure Index (DR) - AGFA

## Slide 35: Exposure Index (DR) - AGFA

## Slide 36: Exposure Index (DR) - AGFA

## Slide 37: Exposure Index (DR) - AGFA

## Slide 38: Exposure Index (DR) - AGFA